Alternate Multiplex Interrupt Specification Library
Public Domain 1992 Ralf Brown
Version 0.83
LastEdit: 5/2/92

Files in this library:
	AMISLIB.DOC	this file
	TSRS.DOC	usage instructions for sample TSRs and utilities
	AMIS.MAC	include file defining various macros
	AMIS.ASM	the actual library code
	AMITSRS.C	sample program to list resident programs using AMIS
	FINDTSRS.C	function to find all TSRs matching a given name
        POPUP.C         sample program to request popup of an AMIS TSR
	REMOVE.C	sample program to remove a specific AMIS TSR
	UNINSTAL.ASM	TSR remover for REMOVE.C
	FASTMOUS.ASM	sample TSR
	NOLPT.ASM	sample TSR -- turn parallel port into bit bucket
	SWITCHAR.ASM	sample TSR -- provide switchar() for MSDOS 5.0
	VGABLANK.ASM	sample TSR -- VGA screen blanker
	NOTE.ASM	sample TSR -- popup note-taker
	MAKEFILE	make all programs from the library sources

------------------------------------------------------------------------

Advantages of AMISLIB:

	totally free
	adds only 1K to the executable -- TSRs can be less than 1.4K on
	  disk and as little as 128 bytes in memory
        up to 256 AMIS-compliant TSRs can be resident simultaneously
          with no interrupt conflicts
	resultant TSR can load itself into high memory (either MSDOS 5
	  upper memory blocks or XMS upper memory blocks); the user has
	  control over where TSR is allowed to load: high only, low only,
	  or high first then low; high memory may use either the first or
	  the best UMB; low memory may use either the low end or the high
	  end of conventional memory.
	TSRs using AMISLIB or other AMIS-compliant code can be unloaded
	  in any order, and can be unloaded by programs other than the
	  TSR's original executable

Note: This is still a preliminary version of the library, so there might
      be problems.  Please let me know if you find any....

------------------------------------------------------------------------

To make use of this library, you basically need to do three things:

	1. To each source file that will make calls, add
		INCLUDE AMIS.MAC
	2. If using a memory model other than Tiny, you must provide a
	   public word variable '__psp' (in C, '_psp'--Turbo C provides
	   this automatically) whose contents are the PSP segment of
	   the program.
	3. Link in AMIS.OBJ (assembled from AMIS.ASM) with the rest of
	   your object modules.

Limitations:
	The ALTMPX and INSTALL_TSR macros must be invoked from the same
	source file in order for the installer to properly fix up the
	resident AMIS handler.	(If not, you will have to perform the
	fixup yourself in an 'init' handler for INSTALL_TSR)

------------------------------------------------------------------------

After an INCLUDE AMIS.MAC, the following definitions and macros are available:

AMIS_VERSION
    100 times the version of the specification to which the library
    conforms (i.e. 123 = version 1.2.3).

AMISLIB_VERSION
    100 times the version of this library

RESIDENT_CODE
    The name of the segment to ASSUME or use in overrides when accessing
    data within the part of the program which will remain resident.

TGROUP
    Group containing all resident segments in the TSR.	See also TSRgroup@.

TSRcode@
TSRcodeEnd@
    Delimit the code which will remain resident; some of the other
    macros listed below will not function correctly unless within a
    section of code delimited with TSRcode@ and TSRcodeEnd@.

TSRdata@
TSRdataEnd@
    Delimit the initialized data which will remain resident.  Requires the
    use of TSRgroup@ to function properly.

TSRbss@
TSRbssEnd@
    Delimit the uninitialized data which will be placed in the resident
    portion (but omitted from the disk image of the executable if
    possible).	Requires the use of TSRgroup@ to function properly.

TSRgroup@
    Declare TGROUP and force the correct ordering of TSRcode@, TSRdata@,
    and TSRbss@.

DISPLAY_STRING
    Output a '$'-terminated string to standard output via DOS.
    Usage:
	DISPLAY_STRING string,dataseg
    Arguments:
	string	the label of the string to be displayed
	dataseg [opt] the segment of the string
    Example:
	DISPLAY_STRING banner
	...
	...
	banner db "FOOBAR (c) 1992 Harry Q Bovik",13,10,"$"

CHECK_DOS_VER
    Ensure that the program is running under the proper version of DOS,
    and terminate with an error message specifying the minimum required
    version if not.
    Usage:
	CHECK_DOS_VER  major,minor
    Example:
	CHECK_DOS_VER 2,00

IF_INSTALLED
    Conditionally branch somewhere if the TSR is already installed.
    Usage:
	IF_INSTALLED rescode,rtype,dest
    Arguments:
	rescode	 segment of TSR code within executable (to get signature
		 and hook list)
	rtype	 type of segment reference: REL = paras offset from CS
					    RELBYTE = bytes offset from CS
					    ABS = absolute segment number
	dest	 label to branch to if already installed
    Return:
	falls through with CF clear if not already installed
	branches with CF set and AH = multiplex number if installed

INSTALL_TSR
    Allocate memory for the resident code, copy the resident code to the
    allocated memory, hook all interrupts used by the TSR, optionally
    call an initialization function, and terminate back to DOS.
    Usage:
	INSTALL_TSR loc,ltype,siz,stype,extra,fit,high,init,if_inst,on_err,
		    more_flags
    Arguments:
	loc	location of resident code
	ltype	type of above location: REL = para offset from CS
					RELBYTE = bytes offset from CS
					ABS = absolute paragraph number
	siz	size of resident code
	stype	type of above size: BYTE or PARA
	extra	[opt] number of additional paragraphs needed in resident part
	fit	[opt] FIRST or BEST (default) -fit allocation
	high	[opt] HIGHONLY to only use UMBs, LOWONLY to only use
			conventional memory, TOPMEM to allocate block at high 
			end of conventional memory if no UMBs, TOPLOW
			to only use top end of conventional memory
	init	[opt] function to call after installing TSR but before exiting
	if_inst [opt] label to branch to if already installed
	on_err	[opt] label to branch to if unable to install
	more_flags [opt] label of byte containing additional flags to be ORed
		   with those automatically set by <fit> and <high>
    Notes:
	If 'init' is specified, the indicated function will be called with
	    AX = segment at which TSR was loaded
	If 'if_inst' is specified, the indicated function will be jumped at
	    with
	    AH = multiplex number
	    CX = version number
	The TOPMEM and TOPLOW options are reported to be incompatible with
	    Windows 3.0, and will most likely cause a crash if the TSR is
	    installed while shelled out from a program using SPAWNO or
	    another swapping spawn() replacement.  Then again, anyone who
	    attempts to install a TSR while shelled out of another program
	    deserves whatever happens.

UNINSTALL
    Remove the TSR from memory.
    Usage:
	UNINSTALL rescode,rtype,on_err
    Arguments:
	rescode	  segment of TSR code within executable (to get signature
		  and hook list)
	rtype	  type of segment reference: REL = paras offset from CS
					     RELBYTE = bytes offset from CS
					     ABS = absolute segment number
	on_err	  [opt] label to branch to if unable to remove from memory
    Notes:
	If 'on_err' is omitted, check CF after this macro to determine
	whether the removal was successful (CF clear if successful, set
	on error).

ISP_HEADER
    Set up the Interrupt Sharing Protocol header for an interrupt.
    Usage:
	ISP_HEADER intr,reset,eoi
    Arguments:
	intr	interrupt number
	reset	[opt] name of routine to perform hardware reset
	eoi	[opt] if nonzero, this is the primary handler for a hardware int
    Exported Labels: (for example "ISP_HEADER 00h,reset_func,0")
	INT00h_handler (public), ORIG_INT00h (public), HWRESET_00h,
	EOI_FLAG_00h
	[in addition, hw_reset_00h would be present for ISP_HEADER 00h,,0]
    Note:
	This macro must be used inside a TSRcode@/TSRcodeEnd@ pair.
    Example:
    	ISP_HEADER 21h
		cmp	ah,4Bh	; provide our own EXEC replacement
		je	exec_call
		jmp	ORIG_INT21h
	exec_call:
		...

HOOKED_INTS
    Declare the interrupts this TSR hooks.
    Usage:
	HOOKED_INTS  int1,int2,...,int32
    Arguments:
	up to 32 interrupt numbers
    Exported Labels:
	HOOKED_INT_LIST (public)
    Notes:
	This macro must be used inside a TSRcode@/TSRcodeEnd@ pair.
	INT 2Dh need not be listed, as it is automatically added to the
	end of the list of hooked interrupts.
    Examples:
    	HOOKED_INTS		; this TSR hooks only INT 2Dh
	HOOKED_INTS 13h,21h,FFh	; this TSR hooks INTs 13h, 21h, 2Dh, FFh

ALTMPX
    Define the alternate multiplex interrupt handler for the program.
    Usage:
	ALTMPX manuf,prodname,version,descrip,priv,api,popup,remove,psp
    Arguments:
	manuf	   one- to eight-character manufacturer's name
	prodname   one- to eight-character product name
	version	   four-digit hex version number (hi byte = major, lo = minor)
	descrip	   [opt] string (max 63 char) describing the product
	priv	   [opt] name of routine to handle private INT 2Dh functions
	api	   [opt] name of FAR routine giving non-INT 2Dh API entry point
	popup	   [opt] name of function to call to request a popup
	remove	   [opt] name of function to call to remove TSR from memory
	psp	   [opt] if nonblank, set up patch word for memblk segment to
			 be returned if <remove> omitted; returns CS if both
			 <remove> and <psp> blank (in this case, INSTALL_TSR
			 must specify either TOPMEM or HIGHONLY)
    Limitations on Routines:
	<priv>	must be located in TSRcode@
		input:	AL = function number (10h-FFh)
			AH = multiplex number (ignore)
			others available for handler
		return: via IRET, with regs as appropriate for requested func
	<api>	must be located in TSRcode@
		input:	registers as desired (no limitations)
		return: registers as desired (no limitations)
	<popup> must be located in TSRcode@
		input:	nothing
		return: AL = status
				01h can not pop up now, try again later
				02h can not pop up yet, will do so when able
				03h already popped up
				04h unable to popup, user intervention required
				    BX = standard reason code
					0000h unknown failure
					0001h int chain passes through memory
						which must be swapped out
					0002h swap-in failed
				    CX = application's reason code if nonzero
				FFh TSR popped up and was exited by user
				    BX = return value
					0000h no return value
					0001h TSR unloaded
					0002h-00FFh reserved
					0100h-FFFFh application-specific
	<remove> must be located in TSRcode@
		input:	DX:BX = return address if uninstall successful
		return: AL = status
				01h unable to remove from memory
				02h can't remove now, will do so when able
				03h safe to remove, but no resident uninstaller
				    (TSR still enabled)
					BX = segment of memory block
				04h safe to remove, but no resident uninstaller
				    (TSR now disabled)
					BX = segment of memory block
				05h not safe to remove now, try again later
				FFh successful (DX:BX were ignored)
		return at DX:BX with AX destroyed if successful and <remove>
			honors specific return address
		if <remove> omitted, ALTMPX returns AL=03h
    Exported Labels:
	INT2Dh_handler (public), ORIG_INT2Dh (public), HWRESET_2Dh,
	EOI_FLAG_2Dh, hw_reset_00h, MULTIPLEX_NUMBER (public),
	ALTMPX_SIGNATURE (public), ALTMPX$PSP [patch word if <psp> nonblank]
    Note:
	This macro must be used inside a TSRcode@/TSRcodeEnd@ pair.

------------------------------------------------------------------------

For more details, see AMIS.MAC, AMIS.ASM, and the source to the example
TSRs.  See also TSRS.DOC for usage information on the sample TSRs.

------------------------------------------------------------------------

	Ralf Brown
	School of Computer Science
	Carnegie Mellon University
	Pittsburgh, PA 15213-3890

	Ralf Brown 1:129/26.1
	ralf+@cs.cmu.edu